## Slide 1
1
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Acceleration of
Graph Attention Network
on FPGA
Computer Engineering Project
---oOo---
Council: CE - CC05
Supervisor: Assoc. Prof. Pham Quoc Cuong
Member Secretary: Mr. Nguyen Thanh Loc
Authors:
  Hoang Tien Duc - 2152520
  Dang Hoang Gia - 2153312
  Nguyen Duc Bao Huy - 2152089
Notes: G morning every one,
This is Gia and our team member Duc Huy
I will present our Computer Engineering project about Acceleration of Graph Attention Network on FPGA.

## Slide 2
2
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Outline
01. Introduction
03. Methodological Approach
04. Overall Architecture
05. Implementation
06. Result
02. Background

## Slide 3
Introduction
3
01

## Slide 4
4
GCN:
  Used in tasks like node classification and link prediction
  But poor performance on dynamic and inductive tasks.
GAT:
  Improves flexibility with an attention mechanism, focusing on important node relationships,
  Make it better for complex, dynamic, and real-time tasks.
==> FPGA-based accelerators for GAT are needed to accelerate the computation of GAT operations.
.
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Graph Neural Network
Notes: Graph Convolutional Network
or to say Convolutional Network in graph structure
but may result in poor performance in some specific dataset of inductive task.
GRAPH ATTENTION NETWORK

## Slide 5
Background
5
02

## Slide 6
6
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
ZCU106 Zynq SoC Ultrascale+
Zynq UltraScale+ MPSoC ZCU106
Resource on XCZU7EV
Notes: our experiment is plan to implemented on ZCU Soc Ultrascale+
with a large resource of LUT and Block RAM

## Slide 7
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
PYNQ Processing System
Pynq Framework
Xilinx PS-PL Connectivity

## Slide 8
7
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Graph Attention Network
GAT Algorithms:
Linear transformation:
Attention coefficient:
Softmax:
Aggregation:
Notes: We list out 4 formula for a graph attention layer, which are

## Slide 9
8
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Graph Attention Network
Weight and feature linear transformation
Notes: In the figure, each row of matrix H will be a vector to perform linear transformation with Weight matrix W.
for example in this case, 5 rows of matrix H with 4 features value will multiply with 4x8 W matrix.
the result will be 4 vector z with size 8.

## Slide 10
9
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Graph Attention Network
Attention coefficient
Notes: attention means to define the importance of the connected node in the graph.
there will be learnable attention weight, and we have to concatenate z values of 2 connected node to multiply them.

## Slide 11
10
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Graph Attention Network
Softmax
Notes: Softmax normalizes the result into a probability distribution.
The reason of softmax is to classify, score the importance of edges
in this case
attention coefficient in each edge of neighboring nodes will be normalized.

## Slide 12
11
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Graph Attention Network
Aggregation
Notes: Final calculation of a GAT layer is aggregating all the previous calculations to return the output of the layer.
GAT layer result will be the sum of Weighted features, combine with attention coefficient.
To control output range, there will an activation function applied to the aggregated result.

## Slide 13
12
S-GAT: (W. Yan, W. Tong and X. Zhi)
  Model compression, feature quantization, shift-based multiplication.
  Performance: 593x CPU, 7.34x Nvdia Tesla V100
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Related Work
SH-GAT: (Wang. et.al)
  Split weights, softmax approximation, load-balanced SPMM, pre-fetching to address memory irregularities.
  Performance: 3283x CPU. 13x GPU

## Slide 14
Methodological
Approach
13
03

## Slide 15
14
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Algorithm Optimization
Notes: To implement in hardware, We need to adjust somecalculations to optimize resource and calculation processes.
All Activation functions should change to ReLU in order to avoid negative values.
the concatenation in attention coefficient needs to change to the sum of splitted attention weights. to avoid repetitive multiplication of the z and a.
exponential with base e will be changed to base 2 to gain benefits from shift bit operation in hardware.
Hence, all this modification have to be validate and evaluate system accuracy.

## Slide 16
15
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Data pre-processing
Pipeline stalls occur due to unorganized data flow through computational modules.
==> Group source node and neighboring nodes into a subgraph to streamline data flow and prevent stalls.
Notes: Unstructured data of input feature matrix will result in unstructured data through some calculation module.
Hence, some processes have to wait for values to finish computing for a long time,may cause some pipeline stalls issue.
we propose to organize data in the beginning before transfer to hardware implementation. therefore all related node can be grouped together and finish calculating at the same time in each module block.

## Slide 17
16
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Data pre-processing
A 4-node graph can represent as 4 subgraphs.
Source node: header of each subgraph.
Neighbor node: node adjacent to source node.
Notes: We proposed to group connected node into subgraphs, with source node and the neighboring node.
in this example, 4 node graph can represent as 4 subgraphs.
source node: will be at head.
while other connected node is followed.

## Slide 18
17
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
GCSR Format
GCSR stands for Graph Compressed Sparse Row.
  Collect information of index and value, compressed it into 3 components.
  Organized by subgraphs.
Notes: Graph Compressed Sparse Row
We introduce a new format for graph representation, by collect information of non-zero value in the feature subgraphs.
info can be extract in 3 array:
col index column index of value
value
node_info: comprise of row length (how many non-zero value in subgraph), num_of_nodes in subgraphs, node_flag indicate source node.

## Slide 19
Overall Architecture
18
04

## Slide 20
19
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
General Architecture
PS is responsible for running software application (training GAT model and transferring input data).
PL is responsible for operating GAT algorithm.
  Memory Controller (6 BRAMs).
  Scheduler (3 Loaders).
  SPMM (Sparse Matrix Multiplication).
  DMVM (Dense Matrix Vector Multiplication).
  Softmax.
  Aggregator.

## Slide 21
20
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
SPMM/SP-PE
(Sparse Matrix Vector Multiplication/Sparse Processing Element)
Each SP-PE contains a column-specific Weight BRAM.
col_idx is used as read address to retrieve the corresponding weight value from BRAM.
When the number of non-zero feature values reaches row_length, pe_ready_o will be asserted.

## Slide 22
21
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
DMVM
(Dense Matrix Vector Multiplication)
Each WH entry is multiplied with either a_source or a_neighbor based on src_flag.
The result is then concatenated with the source node's product.
Finally, it passes through the ReLU function to retrieve Attention Cofficient e.

## Slide 23
22
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Softmax
Each entry from e BRAM contains attention coefficients of a subgraph.
After calculating the base-2 exponentials for each coefficient, their sum is computed sequentially.
Finally, each base-2 exponential coefficient is divided by the sum to obtain the normalized coefficient.

## Slide 24
23
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Aggregator
Each vector from WH BRAM is multiplied with corresponding normalized coefficient from α BRAM.
The results are accumulated until all nodes in the subgraph are processed.
Finally, the accumulated values pass through the ReLU function to produce the feature vector for the next layer.

## Slide 25
Implementation
24
05

## Slide 26
25
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
System Implementation
System Block Design (Vivado)

## Slide 27
Results
26
06

## Slide 28
27
Feature (4x5)
Weight (5x6)
WH (4x6)
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
SPMM Simulation
col_idx
value
node_info

## Slide 29
28
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
SPMM Simulation

## Slide 30
29
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
SPMM Simulation
Calculation operation in one SP-PE module

## Slide 31
30
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Model Training
3-D Visualization
Visualize Cora Dataset (Without Training)
2-D Visualization

## Slide 32
31
82.5%
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Model Training
3-D Visualization
Visualization (Training GAT Model + Without Quantization)
2-D Visualization
Accuracy

## Slide 33
32
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Model Training
3-D Visualization
Visualization (Training GAT Model + Quantization)
2-D Visualization
Accuracy
82.2%

## Slide 34
Future Plan
33

## Slide 35
34
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Future Plan
Proposed Timeline And Goals

## Slide 36
Thank you for your Attention
35

## Slide 37
36
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
System Accuracy
3-D Visualization
Visualization (Full Flow Simulation On Software)
2-D Visualization
Accuracy
82.2%

## Slide 38
37
Quantization Process
  Convert parameters from Float32 to Int8
  Apply Quantization Aware Training (QAT) technique
  Detailed Flow

## Slide 39
38
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Softmax Accuracy Loss
Accuracy loss across datasets

## Slide 40
39
Ho Chi Minh University of Technology
Faculty of Computer Science and Engineering
Computer Engineering Project | 2024
Latency Comparison
Comparison with FPGA-based accelerators on latency

## Slide 41
40
GAT With Dataset
  Cora (Previous Slide)
  CiteSeer
  PubMed
Dataset information with Nodes, Edges and Features